| Action | Sign | Date |
| --- | --- | --- |
| Entered and Uploaded to Training Matrix |  |  |

# Name of Candidate:	____________________

# Date:	 	_____ / _____ / _______

# Conditions of Assessment

Before assessment, the Candidate should have read, be familiar with and signed off the:

-	FO6236 – Isolation Written Assessment

-	SOP3026 – Isolation

# Candidates must have passed the written questions with a 100% pass mark

# Before attempting the practical assessment

# Practical Assessment

# The Inductor for a practical assessment can only be performed by:

# Personnel who have a clear understanding of the Isolation requirements for Mobile Equipment

# Hold a current competency for that area of work.

# Candidates sign for their locks on FO3111 with the understanding

# that they are for their use whilst employed with Big Yellow.

- The candidate must follow the SOP3026 Isolation procedure for isolating and de-isolating an item of equipment or plant for pre-start inspection, servicing or maintenance.

- The candidate must demonstrate safe work practices at all times and comply with the following critical requirements.

- Candidates should complete a Big Yellow Take 5 Assessment before commencing the isolation practical assessment

- When Practical Assessment is complete, the Site Trainer Assessor must check and sign off the document, before entering and uploading to the training register

The Inductor shall observe the candidate undertake isolation and de-isolation of plant / equipment in the following relevant scenarios:

- Isolation of plant / equipment in working as an individual

- Isolation of plant / equipment in working with another person

The Inductor should respond to the following questions in observation of the Isolation process:

- Is the machine correctly parked up for undertaking inspections	Yes / No

- In V-drain with park brake applied

- In a level area with park brake set and chocked (front and rear of wheel)

- Ground engaging tools secure

- Did candidate check that the cab and area around the equipment is clear	Yes / No

- Has candidate attached Personal Lock and Danger Tag to the relevant isolation point. 	Yes / No

- Did the candidate check the effectiveness of the isolation.	Yes / No

- Upon de-isolation, did the candidate undertake the correct requirements for the tags	Yes / No

Inductor is required to ask the following questions and clearly note the candidates responses.

If short term maintenance is required in the pit or go-line for equipment, where should the operator be positioned before maintenance is commenced?

If the operator is required to operate equipment to test for maintenance result, are they required to tag onto the equipment? If Yes, which tag do they need to complete?

If the risk level is HIGH or CATASTROPHIC, do not start work

- see your Supervisor

|  | CONSEQUENCE |
| --- | --- |
| LIKELIHOOD | 1 (Insignificant) | 2 (Minor) | 3 (Moderate) | 4 (Major) | 5 (Catastrophic) |
| A - (Almost Certain) | M (15) | H (10) | E (6) | E (3) | E (1) |
| B - (Likely) | M (19) | H (14) | H (9) | E (5) | E (2) |
| C - (Possible) | L (22) | M (18) | H (13) | E (8) | E (4) |
| D - (Unlikely) | L (24) | L (21) | M (17) | H (12) | E (7) |
| E - (Rare) | L (25) | L (23) | M (20) | M (16) | H (11) |

Assessment Summary

# Conditions of Assessment

As part of this assessment, the Candidate should have been shown, have read and be familiar with the current versions and have signed off on:

Candidate to Sign

-	FO6236B – Isolation Written Assessment	_____

-	SOP3026 – Isolation	_____

-	I have been provided with a personal lock/danger tag for my use whilst working at Big Yellow	_____

Acknowledgement of Inductor / Assessor

# CommentS / FEEDBACK:

Did the candidate do a Take 5 Assessment before commencing isolation practical assessment 	Yes / No

At the time of assessment the candidate below is deemed Competent □  Not Yet Competent □ after successful completion of the written and practical assessment

____ / ____ / ________

Name - Inductor / Assessor	Signature - Inductor / Assessor	Date

Reassessment due 3 years from this date

Trainer Assessor is required to sign off confirming the written and practical assessments are complete and signed off by all involved parties

____ / ____ / ________

Name – Trainer Assessor	Signature – Trainer Assessor	Date

Acknowledgement of Candidate

I acknowledge the assessment result and the Inductor / Assessor’s comments

____ / ____ / ________

Name - Candidate	Signature - Candidate	Date

Acknowledgement of Project / Alternate Manager

At time of signing, I acknowledge the assessment process has been followed:

Candidate is deemed as being (tick applicable response):

□	Competent - can safely and confidently apply these skills to the task

□	Not Yet Competent - will need to continue in the training process.

____ / ____ / ________

Name - Project/Alternate Manager	Signature - Project/Alternate Manager	Date